SiS

SP300/305

3D GRAPHIC

ACCELERATOR

MANUAL

Table of Content

1.	SiS 300/305	1

1.1	SiS 300 /305 Features	1

1.2	SiS300/305 Board Outline	2

2.	Mode Tables	3

2.1	Standard VGA Modes	3

2.2	Enhanced Video Modes	5

2.3	Low Resolution Modes (Hidden)	9

3.	Hardware Installation	10

3.1	Package Contents	10

3.2	Installing the Card	10

4.	Smart Installation	11

For Windows 95 OSR2.1, Windows 98, WindowsNT4.0 SP3 or newer	11

5.	Manually install Windows 95 & Windows 98 drivers	12

5.1	Installation and Setup	12

5.1.1	Windows95	12

5.1.2	Windows98	12

5.1.3	How to Change Color Depth and Resolution	13

5.1.4	How to Change Refresh Rate	13

5.1.5	Windows 2000	13

FCC Statement	15

Warning:	15

Trademark Acknowledgments	15

# SiS 300/305

## SiS 300 /305 Features

AGP Interface

- Support AGP 2.0 compliant configuration setting

- SiS 300 Support AGP 4X 266 MHz with maximum 32 stages pipeline full side band function

- SiS 305 Support AGP 2X 133MHz with maximum 32 stages pipeline full side band function

High Performance & High Quality 3D Accelerator

- Built-in a high performance 128-bit 3D engine

- Built-in a high quality 3D engine

High Performance 2D Accelerator

- Supports Turbo Queue(software Command Queue in off-screen memory)architecture to achieve

extra-high performance(SiS patent)

- Built-in Direct Draw Accelerator

- Built-in an 1T 64-bit BITBLT graphics engine

- Supports memory-mapped, zero wait-state, burst engine write

- Support burst frame buffer read/write for SDRAM/SGRAM

- Built-in 64x64x2 bit-mapped color hardware cursor

- Built-in 32x32x16, 32x32x32 bit-mapped color hardware cursor

- SiS 300 Maximum 64MB frame buffer with linear addressing

- SiS 305 Maximum 32MB frame buffer with linear addressing

- Supports AGP 2X mode access fro all 2D engine functions

Display Memory Interface

-SiS 300 Support 8/16/32/64MB memory configuration

-SiS 305 Support 8/16/32MB memory configuration

- Support VGA BIOS auto memory size detecting

High integration

- Built-in CRT FIFOs to support super high resolution graphics modes and reduce CPU wait-state

- Built-in programmable 24-bit true-color RAMDAC up to 270MHz pixel clock

- Built-in three clock generators

- Built-in two video line buffers for MPEG II video playback

- Built-in standard feature connector logic support

Supports super high resolution graphics modes

- 640x480		16/256/32K/64K/16M colors 120Hz NI

- 800x600		16/256/32K/64K/16M colors 120Hz NI

- 1024x768		256/32K/64K/16M colors 120Hz NI

- 1280x1024		256/32K/64K/16M colors 85 Hz NI

- 1600x1200		256/32K/64K colors 100Hz NI

- 1920x1440		256/32K/64K colors 70Hz NI

## SiS300/305 Board Outline

FC PROT

DB15

BIOS     14.318Mhz

AGP 2.0

# Mode Tables

## Standard VGA Modes

| MODE | TYPE | DISPLAY SIZE | COLORS SHADES | ALPHA FORMAT | BUFFER START | BOX SIZE | MAX. PAGES |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | A/N | 320x200 | 16 | 40x25 | B800 | 8x8 | 8 |
| 0* | A/N | 320x350 | 16 | 40x25 | B800 | 8x14 | 8 |
| 0+ | A/N | 360x400 | 16 | 40x25 | B800 | 9x16 | 8 |
| 1 | A/N | 320x200 | 16 | 40x25 | B800 | 8x8 | 8 |
| 1* | A/N | 320x350 | 16 | 40x25 | B800 | 8x14 | 8 |
| 1+ | A/N | 360x400 | 16 | 40x25 | B800 | 9x16 | 8 |
| 2 | A/N | 640x200 | 16 | 80x25 | B800 | 8x8 | 8 |
| 2* | A/N | 640x350 | 16 | 80x25 | B800 | 8x14 | 8 |
| 2+ | A/N | 720x400 | 16 | 80x25 | B800 | 9x16 | 8 |
| 3 | A/N | 640x200 | 16 | 80x25 | B800 | 8x8 | 8 |
| 3* | A/N | 640x350 | 16 | 80x25 | B800 | 8x14 | 8 |
| 3+ | A/N | 720x400 | 16 | 80x25 | B800 | 9x16 | 8 |
| 4 | APA | 320x200 | 4 | 40x25 | B800 | 8x8 | 1 |
| 5 | APA | 320x200 | 4 | 40x25 | B800 | 8x8 | 1 |
| 6 | APA | 640x200 | 2 | 80x25 | B800 | 8x8 | 1 |
| 7 | A/N | 720x350 | 4 | 80x25 | B000 | 9x14 | 8 |
| 7+ | A/N | 720x400 | 4 | 80x25 | B000 | 9x16 | 8 |
| 0D | APA | 320x200 | 16 | 40x25 | A000 | 8x8 | 8 |
| 0E | APA | 640x200 | 16 | 80x25 | A000 | 8x8 | 4 |
| 0F | APA | 640x350 | 2 | 80x25 | B000 | 8x14 | 2 |
| 10 | APA | 640x350 | 16 | 80x25 | A000 | 8x14 | 2 |
| 11 | APA | 640x480 | 2 | 80x30 | A000 | 8x16 | 1 |
| 12 | APA | 640x480 | 16 | 80x30 | A000 | 8x16 | 1 |
| 13 | APA | 320x200 | 256 | 40x25 | A000 | 8x8 | 1 |

# NOTE:	1. A/N: Alpha/Numeric

# 2. APA: All Point Addressable (Graphics)

| MODE | DISPLAY SIZE | COLORS SHADES | FRAME RATE. | H-SYNC. | VIDEO FREQ. |
| --- | --- | --- | --- | --- | --- |
| 0 | 320x200 | 16 | 70 | 31.5 K | 25.1 M |
| 0* | 320x350 | 16 | 70 | 31.5 K | 25.1 M |
| 0+ | 360x400 | 16 | 70 | 31.5 K | 28.3 M |
| 1 | 320x200 | 16 | 70 | 31.5 K | 25.1 M |
| 1* | 320x350 | 16 | 70 | 31.5 K | 25.1 M |
| 1+ | 360x400 | 16 | 70 | 31.5 K | 28.3 M |
| 2 | 640x200 | 16 | 70 | 31.5 K | 25.1 M |
| 2* | 640x350 | 16 | 70 | 31.5 K | 25.1 M |
| 2+ | 720x400 | 16 | 70 | 31.5 K | 28.3 M |
| 3 | 640x200 | 16 | 70 | 31.5 K | 25.1 M |
| 3* | 640x350 | 16 | 70 | 31.5 K | 25.1 M |
| 3+ | 720x400 | 16 | 70 | 31.5 K | 28.3 M |
| 4 | 320x200 | 4 | 70 | 31.5 K | 25.1 M |
| 5 | 320x200 | 4 | 70 | 31.5 K | 25.1 M |
| 6 | 640x200 | 2 | 70 | 31.5 K | 25.1 M |
| 7* | 720x350 | 4 | 70 | 31.5 K | 28.3 M |
| 7+ | 720x400 | 4 | 70 | 31.5 K | 28.3 M |
| 0D | 320x200 | 16 | 70 | 31.5 K | 25.1 M |
| 0E | 640x200 | 16 | 70 | 31.5 K | 25.1 M |
| 0F | 640x350 | 2 | 70 | 31.5 K | 25.1 M |
| 10 | 640x350 | 16 | 70 | 31.5 K | 25.1 M |
| 11 | 640x480 | 2 | 60 | 31.5 K | 25.1 M |
| 12 | 640x480 | 16 | 60 | 31.5 K | 25.1 M |
| 13 | 320x200 | 256 | 70 | 31.5 K | 25.1 M |

# NOTE:	i - interlaced mode

# n - noninterlaced mode

## Enhanced Video Modes

| MODE | TYPE | DISPLAY SIZE | COLORS SHADES | ALPHA FORMAT | BUFFER START | BOX SIZE | MAX. PAGES |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25 | APA | 640x480 | 16 | 80x60 | A000 | 8x8 | 1 |
| 29 | APA | 800x600 | 16 | 100x37 | A000 | 8x16 | 1 |
| 2D | APA | 640x350 | 256 | 80x25 | A000 | 8x14 | 1 |
| 2E | APA | 640x480 | 256 | 80x30 | A000 | 8x16 | 1 |
| 2F | APA | 640x400 | 256 | 80x25 | A000 | 8x16 | 1 |
| 30 | APA | 800x600 | 256 | 100x37 | A000 | 8x16 | 1 |
| 31 | APA | 640x400 | 64k | 80x50 | A000 | 8x16 | 1 |
| 38 | APA | 1024x768 | 256 | 128x48 | A000 | 8x16 | 1 |
| 3A | APA | 1280x1024 | 256 | 160x64 | A000 | 8x16 | 1 |
| 3C | APA | 1600x1200 | 256 | 200x75 | A000 | 8x16 | 1 |
| 3D | APA | 1600x1200 | 64k | 200x75 | A000 | 8x16 | 1 |
| 3E | APA | 1600x1200 | 16.8M | 200x75 | A000 | 8x16 | 1 |
| 40 | APA | 320x200 | 32k | 40x25 | A000 | 8x8 | 1 |
| 41 | APA | 320x200 | 64k | 40x25 | A000 | 8x8 | 1 |
| 42 | APA | 320x200 | 16.8M | 40x25 | A000 | 8x8 | 1 |
| 43 | APA | 640x480 | 32k | 80x30 | A000 | 8x16 | 1 |
| 44 | APA | 640x480 | 64k | 80x30 | A000 | 8x16 | 1 |
| 45 | APA | 640x480 | 16.8M | 80x30 | A000 | 8x16 | 1 |
| 46 | APA | 800x600 | 32k | 100x37 | A000 | 8x16 | 1 |
| 47 | APA | 800x600 | 64k | 100x37 | A000 | 8x16 | 1 |
| 48 | APA | 800x600 | 16.8M | 100x37 | A000 | 8x16 | 1 |
| 49 | APA | 1024x768 | 32k | 128x48 | A000 | 8x16 | 1 |
| 4A | APA | 1024x768 | 64k | 128x48 | A000 | 8x16 | 1 |
| 4B | APA | 1024x768 | 16.8M | 128x48 | A000 | 8x16 | 1 |
| 4C | APA | 1280x1024 | 32k | 160x64 | A000 | 8x16 | 1 |
| 4D | APA | 1280x1024 | 64k | 160x64 | A000 | 8x16 | 1 |
| 4E | APA | 1280x1024 | 16.8M | 160x64 | A000 | 8x16 | 1 |
| 62 | APA | 640x480 | 32bpp | 80x30 | A000 | 8x16 | 1 |
| 63 | APA | 800x600 | 32bpp | 100x37 | A000 | 8x16 | 1 |
| 64 | APA | 1280x768 | 32bpp | 128x48 | A000 | 8x16 | 1 |
| 65 | APA | 1280x1024 | 32bpp | 160x64 | A000 | 8x16 | 1 |
| 66 | APA | 1600x1200 | 32bpp | 200x75 | A000 | 8x16 | 1 |
| 67 | APA | 1920x1200 | 256 | 240x75 | A000 | 8x16 | 1 |
| 68 | APA | 1920x1200 | 64k | 240x75 | A000 | 8x16 | 1 |
| 69 | APA | 1920x1200 | 32bpp | 240x75 | A000 | 8x16 | 1 |

# NOTE:	1. APA: All Point Addressable (Graphics)

| MODE | DISPLAY SIZE | COLORS SHADES | FRAME RATE. | H-SYNC. | VIDEO FREQ. |
| --- | --- | --- | --- | --- | --- |
| 25 | 640x480 | 16 | 60 | 31.5k | 25.1M |
| 29 | 800x600 | 16 | 56 | 35.1k | 30.0M |
| 29* | 800x600 | 16 | 60 | 37.9k | 40.0M |
| 29+ | 800x600 | 16 | 72 | 48.0k | 50.0M |
| 29# | 800x600 | 16 | 75 | 46.8k | 50.0M |
| 29## | 800x600 | 16 | 85 | 53.7k | 56.3M |
| 2D | 640x350 | 256 | 70 | 31.5k | 25.1M |
| 2E | 640x480 | 256 | 60 | 31.5k | 25.1M |
| 2E* | 640x480 | 256 | 72 | 37.9k | 31.5M |
| 2E+ | 640x480 | 256 | 75 | 37.5k | 31.5M |
| 2E++ | 640x480 | 256 | 85 | 43.4k | 36.0M |
| 2F | 640x400 | 256 | 70 | 31.5k | 25.1M |
| 30 | 800x600 | 256 | 56 | 35.1k | 36.0M |
| 30* | 800x600 | 256 | 60 | 37.9k | 40.0M |
| 30+ | 800x600 | 256 | 72 | 48.0k | 50.0M |
| 30# | 800x600 | 256 | 75 | 46.8 | 50.0M |
| 30## | 800x600 | 256 | 85 | 53.7k | 56.3M |
| 31 | 640x480 | 64k | 70 | 31.5k | 25.1M |
| 38i | 1024x768 | 256 | 87 | 35.5k | 44.9M |
| 38n | 1024x768 | 256 | 60 | 48.4k | 65.0M |
| 38n+ | 1024x768 | 256 | 70 | 56.5k | 75.0M |
| 38n# | 1024x768 | 256 | 75 | 60.2k | 80.0M |
| 38n## | 1024x768 | 256 | 85 | 68.7k | 94.5M |
| 3Ai | 1280x1024 | 256 | 87 | 48.8k | 80.0M |
| 3An | 1280x1024 | 256 | 60 | 65.0k | 110.0M |
| 3An+ | 1280x1024 | 256 | 75 | 80.0k | 135.0M |
| 3Ci | 1600x1200 | 256 | 87 | 75.6k | 135.0M |
| 3C | 1600x1200 | 256 | 60 | 75.6k | 162.0M |
| 3C* | 1600x1200 | 256 | 65 | 75.6k | 175.5M |
| 3Di | 1600x1200 | 64k | 87 | 75.6k | 135.0M |
| 3D | 1600x1200 | 64k | 60 | 75.6k | 162.0M |
| 3D* | 1600x1200 | 64k | 65 | 75.6k | 175.5M |
| 3Ei | 1600x1200 | 16.8M | 87 | 75.6k | 135.0M |
| 3E | 1600x1200 | 16.8M | 60 | 75.6k | 162.0M |
| 3E* | 1600x1200 | 16.8M | 65 | 75.6k | 175.5M |
| 40 | 320x200 | 32k | 70 | 31.5k | 25.1M |
| 41 | 320x200 | 64k | 70 | 31.5k | 25.1M |
| 42 | 320x200 | 16.8M | 70 | 31.5k | 25.1M |
| 43 | 640x480 | 32k | 60 | 31.5k | 25.1M |
| 43* | 640x480 | 32k | 72 | 37.9k | 31.5M |

| 43+ | 640x480 | 32k | 75 | 37.5k | 31.5M |
| --- | --- | --- | --- | --- | --- |
| 43++ | 640x480 | 32k | 85 | 43.4k | 36.0M |
| 44 | 640x480 | 64k | 60 | 31.5k | 25.1M |
| 44* | 640x480 | 64k | 72 | 37.9k | 31.5M |
| 44+ | 640x480 | 64k | 75 | 37.5k | 31.5M |
| 44++ | 640x480 | 64k | 85 | 43.4k | 36.0M |
| 45 | 640x480 | 16.8M | 60 | 31.5k | 25.1M |
| 45* | 640x480 | 16.8M | 72 | 37.9k | 31.5M |
| 45+ | 640x480 | 16.8M | 75 | 37.5k | 31.5M |
| 45++ | 640x480 | 16.8M | 85 | 43.4k | 36.0M |
| 46 | 800x600 | 32k | 56 | 35.1k | 36.0M |
| 46* | 800x600 | 32k | 60 | 37.9k | 40.0M |
| 46+ | 800x600 | 32k | 72 | 48.0k | 50.0M |
| 46# | 800x600 | 32k | 75 | 46.8k | 50.0M |
| 46## | 800x600 | 32k | 85 | 53.7k | 56.3M |
| 47 | 800x600 | 64k | 56 | 35.1k | 36.0M |
| 47* | 800x600 | 64k | 60 | 37.9k | 40.0M |
| 47+ | 800x600 | 64k | 72 | 48.0k | 50.0M |
| 47# | 800x600 | 64k | 75 | 46.8k | 50.0M |
| 47## | 800x600 | 64k | 85 | 53.7k | 56.3M |
| 48 | 800x600 | 16.8M | 56 | 35.1k | 36.0M |
| 48* | 800x600 | 16.8M | 60 | 37.9k | 40.0M |
| 48+ | 800x600 | 16.8M | 72 | 48.0k | 50.0M |
| 48# | 800x600 | 16.8M | 75 | 46.8k | 50.0M |
| 48## | 800x600 | 16.8M | 85 | 53.7k | 56.3M |
| 49i | 1024x768 | 32k | 87 | 35.5k | 44.9M |
| 49n | 1024x768 | 32k | 60 | 48.4k | 65.0M |
| 49n+ | 1024x768 | 32k | 70 | 56.5k | 75.0M |
| 49n# | 1024x768 | 32k | 75 | 60.2k | 80.0M |
| 49n## | 1024x768 | 32k | 85 | 68.7k | 94.5M |
| 4Ai | 1024x768 | 64k | 87 | 35.5k | 44.9M |
| 4An | 1024x768 | 64k | 60 | 48.4k | 65.0M |
| 4An+ | 1024x768 | 64k | 70 | 56.5k | 75.0M |
| 4An# | 1024x768 | 64k | 75 | 60.2k | 80.0M |
| 4An## | 1024x768 | 64k | 85 | 68.7k | 94.5M |
| 4Bi | 1024x768 | 16.8M | 87 | 35.5k | 44.9M |
| 4Bn | 1024x768 | 16.8M | 60 | 48.4k | 65.0M |
| 4Bn+ | 1024x768 | 16.8M | 70 | 56.5k | 75.0M |
| 4Bn# | 1024x768 | 16.8M | 75 | 60.2k | 80.0M |
| 4Bn## | 1024x768 | 16.8M | 85 | 68.7k | 94.5M |
| 4Ci | 1280x1024 | 32k | 89 | 48.8k | 80.0M |
| 4Cn | 1280x1024 | 32k | 60 | 65.0k | 110.0M |

.

| 4Cn# | 1280x1024 | 32k | 75 | 80.0k | 135.0M |
| --- | --- | --- | --- | --- | --- |
| 4Cn## | 1280x1024 | 32k | 85 | 91.1k | 157.5M |
| 4Di | 1280x1024 | 64k | 89 | 48.4k | 80.0M |
| 4Dn | 1280x1024 | 64k | 60 | 65.0k | 110.0M |
| 4Dn# | 1280x1024 | 64k | 75 | 80.0k | 135.0M |
| 4Dn## | 1280x1024 | 64k | 85 | 91.1k | 157.5M |
| 4Ei | 1280x1024 | 16.8M | 89 | 48.8k | 80.0M |
| 4En | 1280x1024 | 16.8M | 60 | 65.0k | 110.0M |
| 4En# | 1280x1024 | 16.8M | 75 | 80.0k | 135.0M |
| 4En## | 1280x1024 | 16.8M | 85 | 91.1k | 157.5M |
| 62 | 640x480 | 32BPP | 60 | 31.5k | 25.1M |
| 62* | 640x480 | 32BPP | 72 | 37.9k | 31.5M |
| 62+ | 640x480 | 32BPP | 75 | 37.5k | 31.5M |
| 62++ | 640x480 | 32BPP | 85 | 43.4k | 36.0M |
| 63 | 800x600 | 32BPP | 56 | 35.1k | 36.0M |
| 63* | 800x600 | 32BPP | 60 | 37.9k | 40.0M |
| 63+ | 800x600 | 32BPP | 72 | 48.0k | 50.0M |
| 63# | 800x600 | 32BPP | 75 | 46.8k | 50.0M |
| 63## | 800x600 | 32BPP | 85 | 53.7k | 56.3M |
| 64i | 1024x768 | 32BPP | 87 | 35.5k | 44.9M |
| 64n | 1024x768 | 32BPP | 60 | 48.4k | 65.0M |
| 64n+ | 1024x768 | 32BPP | 70 | 56.5k | 75.0M |
| 64n# | 1024x768 | 32BPP | 75 | 60.2k | 80.0M |
| 64n## | 1024x768 | 32BPP | 85 | 68.7k | 94.5M |
| 65i | 1280x1024 | 32BPP | 89 | 48.8k | 80.0M |
| 65n | 1280x1024 | 32BPP | 60 | 65.0k | 110.0M |
| 65n# | 1280x1024 | 32BPP | 75 | 80.0k | 135.0M |
| 65n## | 1280x1024 | 32BPP | 85 | 91.1k | 157.5M |
| 66i | 1600x1200 | 32BPP | 87 | 75.6k | 135.0M |
| 66n | 1600x1200 | 32BPP | 60 | 75.6k | 162.0M |
| 66n+ | 1600x1200 | 32BPP | 65 | 81.3k | 175.5M |
| 66n# | 1600x1200 | 32BPP | 75 | 93.8k | 202.5M |
| 66n## | 1600x1200 | 32BPP | 85 | 106.3k | 229.5M |
| 67 | 1920x1200 | 256 | 60 | 75.6k | 195.0M |
| 67n | 1920x1200 | 256 | 75 | 93.8k | 245.0M |
| 67n# | 1920x1200 | 256 | 80 | 106.3k | 27.0M |
| 68 | 1920x1200 | 64k | 60 | 75.6k | 195.0M |
| 68n | 1920x1200 | 64k | 75 | 93.8k | 245.0M |
| 68n# | 1920x1200 | 64k | 85 | 106.3k | 275.0M |
| 69 | 1920x1200 | 16.8M | 60 | 75.6k | 195.0M |
| 69n | 1920x1200 | 16.8M | 75 | 93.8k | 245.0M |
| 69n# | 1920x1200 | 16.8M | 80 | 106.3k | 270.0M |

91.1k

# NOT75.6 - interlaced mode

# n - noninterlaced mode

For the limitation of memory bandwidth in 1MB DRAM configuration, the following video modes is not supported in 1MB configuration: modes 45*, 45+, 46+, 46#, 47+, and 47#.

## Low Resolution Modes (Hidden)

| MODE | TYPE | DISPLAY SIZE | COLORS SHADES | ALPHA FORMAT | BUFFER START | BOX SIZE | MAX. PAGES |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 50 | APA | 320x240 | 256 | 40x30 | A000 | 8x8 | 1 |
| 53 | APA | 320x240 | 32K | 40x30 | A000 | 8x8 | 1 |
| 56 | APA | 320x240 | 64K | 40x30 | A000 | 8x8 | 1 |
| 51 | APA | 400x300 | 256 | 50x38 | A000 | 8x8 | 1 |
| 54 | APA | 400x300 | 32K | 50x38 | A000 | 8x8 | 1 |
| 57 | APA | 400x300 | 64K | 50x38 | A000 | 8x8 | 1 |
| 52 | APA | 512x384 | 256 | 64x48 | A000 | 8x8 | 1 |
| 55 | APA | 512x384 | 32K | 64x48 | A000 | 8x8 | 1 |
| 58 | APA | 512x384 | 64K | 64x48 | A000 | 8x8 | 1 |

# NOTE:	1. A/N: Alpha/Numeric

# 2. APA: All Point Addressable (Graphics)

# Hardware Installation

## Package Contents

- SiS300 or SiS305 3D Accelerator card.

- CD title or Software diskettes

- This manual.

## Installing the Card

- Turn off your computer.

- Remove the cover of the computer per the owner’s manual.

- Install the card in the AGP bus slots.

- Replace the cover.

# Smart Installation

## For Windows 95 OSR2.1, Windows 98, WindowsNT4.0 SP3 or newer

4.1 Put the DRIVERS CD in your CD-ROM

4.2 Click the Driver installation

3.3 If everything fine, screen will show Confirm Installation window.

Then Select the OK

3.4 Now appears the Driver Confirmation window

Select the Install

(Here the picture shows Voodoo Banshee for example, if your are using

SiS300/305, Driver Confirmation window will show SiS300/305 drivers)

3.5 Then restart your computer.

# Manually install Windows 95 & Windows 98 drivers

## Installation and Setup

### Windows95

The Windows setup program installs and modifies all of the necessary files. Follow these steps to install the Windows 95 drivers.

- Insert the DISC (CD Title Driver).

- Select Control Panel from My Computer group.

- Select the Display icon

- Double-click on the Display icon in the Setting -> Control Panel folder. You can also click the right mouse button anywhere on the desktop and select the Properties option form the pop-out menu.

- Click the Settings tab.

- Click the change Display Type button.

- Click the Have Disk button.

- Change directories and Select sis300m.inf.(s3savage.inf)

# Disc (CD Title) is E:\drivers\SiS\300/305\WIN95

Note: “E:”-> CD Drive “SiS”-> VGA chip brand name “300/305”-> VGA model name

- Select AGP driver form the list and click the OK button. If a message stating that one or more driver files is older than the files on the system respond YES to overwrite the files.

- Click the Close button and Apply button, and restart your computer.

### Windows98

The Windows setup program installs and modifies all of the necessary files. Follow these steps to install the Windows 98 drivers.

- Insert the DISC (CD Title Driver).

- Select Control Panel from My Computer group.

- Select the Display icon

- Double-click on the Display icon in the Setting -> Control Panel folder. You can also click the right mouse button anywhere on the desktop and select the Properties option form the pop-out menu.

- Click the Settings tab.

- Then show  [Unknown Device.] Properties tab

Select Adapter

- Then show Standard PCI Graphics…. tab

Select Change

- Then show Update Device …. tab

Select Next

- Then show Update Device …. tab

Select Search for a better……

Then select Next.

- Then show Update Device …. tab

If the Specify a location is wrong

Please select Brows

- Then show Browse for Folder tab

Select E:\drivers\ SiS\300/305\win98

# Disc (CD Title) is E:\drivers\ SiS\300/305\WIN95

Note: “E:”-> CD Drive “SiS”-> VGA chip brand name “300\305”-> VGA model name

Then select OK

- Then show Update Device Driver Wizard tab

Select CD-ROM driver

Click the Specify a locator, if right

Then select Next

- Then show Update Device Driver Wizard tab

Select Next

- Then show Update Device Driver Wizard tab

Select Finish

- Then show System Settings Change tab

Select OK

### How to Change Color Depth and Resolution

- Make sure that you have installed windows95/98 Driver.

- Click on the Start box in the lower left corner and proceed to Control Panel.

- Inside the Control panel group , click on Display icon to open the Display Properties folder and select the Setting table

- Click on the pull-down arrow from the Color palette area to select color depth or adjust the sliding bar to either Less or More from the Desktop area

- Select OK to restart WINDOWS95 and new color depth or the new resolution takes effect.

### How to Change Refresh Rate

Here the picture shows Voodoo Banshee for example

- Make sure that you have installed windows95/98 Driver. Click on the Start box in the lower left corner and proceed to Setting, Control Panel

- Inside the Control panel group , click on Display icon to open the Display Properties folder and choose Settings click the Advance Settings choose Adapter

- Click on the Refresh Rate sub window to change refresh rate

- Select OK and new refresh rate takes effect

Note: If your monitor is not Branded or Plug & Play, you will only see Adapter default and optimal. Please contact your monitor supplier to get right or compatible drivers for your monitor. Otherwise you can not select the refresh rate you wanted.

### Windows 2000

First time install drivers under windows2000

- When system boot up, system will prompt find new device. Suppose the device is VGA, now system will find the default drivers for you.

- If you want to install our drivers along with the SP300/SP305 pack. Please put the drivers CD in your CDROM drive. If now shows SmartInstall window, please click EXIT button to quit.

- Drivers for windows2000 are located at \2000drv\sis\300\win2000 or \drivers\sis\300\win2000 (For SP305, please change 300 to 305)

- If the drivers is very new may not certified by Microsoft, if so, system will prompt you the drivers do not have “digital signature”, still you can force to install.

- Follow on screen instructions will finish the installation.

The following steps describe how to update Windows2000 display drivers

- Place the Disc (CD Title) into CDROM Drive. If now shows SmartInstall window, please click EXIT button to quit

- Right click mouse button on Desktop Area, now shows a sub menu window. Please select Properties.

- Now come up Display Properties window, please select Settings on the top.

- Select Advanced

- Select Adapter.

- Select Change

- Now comes up a update drivers wizard window. Please follow the on screen instruction.

- Please specify the drivers location at your CDROM letter: \2000drv\sis\300\win2000 or \drivers\sis\300\win2000 (For SP305, please change 300 to 305) or the directory where you put your drivers

- Select Install and click “YES” when the Installing Driver dialog box appears. If the drivers is very new may not certified by Microsoft, if so, system will prompt you the drivers do not have “digital signature”, still you can force to install.

A message appears stating that drivers were successfully installed. Click OK. Another message appears stating that the driver could not be restarted dynamically. Restart Windows2000 to run the new driver. Click OK.

# FCC Statement

This device complies with part 15 of the FCC Rules. Operation is subject to the following two condition.(1).this device may not cause harmful interference. (2).this device must accept any interference received, including interference that may cause undesired operation

## Warning:

Note: This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to Part 15 of FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, used and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference in to radiate communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna

- Increase the separation between the equipment and receiver.

- Connect the equipment into an outlet on a circuit different form that to which the receiver in connected.

- Consult the dealer or an experienced radio/TV technician for help.

Notice:

(1) An Unshielded-type power cord is required in order to meet FCC emission limits and also to prevent interference to the nearby radio and television reception. It is essential that only the supplied power cord by used.

(2) Use only shielded cables to connect I/O devices to this equipment.3

(3) Changes or modifications not expressly approved by the party responsible for compliance could void the use’s authority to operate the equipment.

# Trademark Acknowledgments

# All brand names and trademarks are the property of their owners.

# Text boxes

Memory

Memory

Memory

SiS

300/305

Memory